## Slide 1
HEVEN OR HELL? GHG IMPLICATIONS OF AN AUTONOMOUS FUTURE
Jennifer Hatch* and Will Gorman^
Economics of Autonomous and Electric Vehicles
National Bureau of Economic Research, Stanford University
June 7th, 2019
* Boston University ^ University of California Berkeley
bu.edu/ise
Notes: Hi everyone, thanks so much for staying for the last presentation of the day! I’ll try and make it interesting. I think the work I’ve been doing brings in a lot of components from the other presentations we’ve seen during this conference, so hopefully you’ll find some value.

## Slide 2
bu.edu/ise
THE THREE REVOLUTIONS IN URBAN TRANSPORTATION
What does it mean for power use?
What do these transformations mean for GHG emissions?
What does this mean for infrastructure needs and city welfare?
How large of a grid will we need?
Will growth return to the power business?
AUTOMATION
SHARING
ELECTRIFICATION
(Sperling, Pike, and Chase, 2018)
Notes: I’m sure all of you have heard of Dan Sperling’s so-called “three revolutions” in transportation: sharing, electrification, and automation.
-bounding the long-term impacts of these transformations in a way that is policy relevant.
-The problem with these transformations is that they each have numerous, difficult to quantify impacts on the light duty fleet.

## Slide 3: PRIOR WORK
Specificity
Time frame for projections
2025
2050
bu.edu/ise
Morgan Stanley (2015)
Goldman
Sachs (2015)
RMI (2016)
Brattle (2016)
BAML (2017)
Makenzie Wadud & Leiby (2014)
World Energy Council (2011)
Stephens et al. (2016)
EPRI/NRDC (2015)
Brown, Gonder, & Repac (2014)
Notes: There have been many prior studies on the subject.
We reviewed a number of them and found that they were either short term in nature, region or city specific, left out one of the disruptions, or produced such wide-ranging results as to be unhelpful for policy guidance.
Our aim is to do a bit better with a more comprehensive forecasting exercise.

## Slide 4
bu.edu/ise
CONCEPTUAL APPROACH
(
)
(
)
(
)
*
*
Number of EVs on the road
Annual Average miles per EV
Energy Intensity
=
EV Power Use
Influenced by ICE-EV competition, policy mandates, vehicle lives, and changes to the “ownership model”
Influenced by development patterns, lifestyle and user preferences, value of time travel, and “ownership model”
Influenced by technological improvements, mandates, and autonomous vehicle penetration
Notes: Our approach is to try and break through this uncertainty by building a stock turnover model based on a kaya identity framework, allowing us to disaggregate the various changes.
Number of Evs on the road (broken down into Evs, Plug ins, ICE, etc.) * VMT * Energy intensity and that gives us EV power use that can then be converted into GHG emissions

## Slide 5
bu.edu/ise
Source: Fox-Penner, Gorman, and Hatch (2018)
Notes: So the paper we published last summer in Energy policy uses this kaya identity framework to examine these three disruptions in a series of layers, disaggregating the VMT, stock, and energy intensity implictions of each layer

## Slide 6: LIFE CYCLE GHG IMPACTS OF AV BUSINESS MODELS
  Q1: We know that EVs are generally more carbon intensive to manufacture; what does this do to our GHG results?
  Q2: autonomous vehicles imply several new potential business models – what impact do those models have on GHGs?
bu.edu/ise
Notes: We use this stock model framework in our new work to answer two questions –
So, the first question I got at the AEA was yes, but what about life cycle?
As we’ll see, that isn’t in itself an interesting question, but it becomes interesting when we start to think about business models – namely, how quickly do these vehicles turn over in each business model and what does that mean for total emissions?

## Slide 7: LIFE CYCLE ANALYSIS
bu.edu/ise
Source: Peters, et al. 2017
Notes: Life cycle analysis: there is this awesome graphic by peters and colleagues that maps out all the LCA work although the literature is quite robust on this subject, there are only a handful of studies from which the data arises: Spoiler – EVs are better for emissions and have been for almost a decade, despite what jonathan lesser says. Anyway, we incorporated life cycle emissions into our model

## Slide 8: INCORPORATING BUSINESS MODELS
  4 main business models, least to greatest hypothesized emissions:
    Sharing/Pooling/Bus  Via, Optimus Ride,
    Taxi/Fleet Model  Uber and Lyft
    Individual Ownership Model  Long-term OEM goal
    Rapid Turnover/Lease Model  Potential long-term as AV evolves
bu.edu/ise
Notes:   4 main business models, least to greatest hypothesized emissions:
    Sharing/Pooling/Bus  Via, Optimus Ride,
    Taxi/Fleet Model  Uber and Lyft
    Individual Ownership Model  Long-term OEM goal
    Rapid Turnover/Lease Model  Potential long-term as AV evolves

## Slide 9
bu.edu/ise
“If we’re not actively monitoring the metric that truly matters –VMT – we could potentially see a future where vehicle ownership goes down, yet VMT (and energy use) go up.”
- Regina R. Clewlow, U.C. Davis
POOLING AND SHARING
Notes: As late as 2015 the TRB was saying that impacts of ridesharing were unknowable. In the last year or two, studies have come out saying that ride-hailing increases VMT up to 60-80% over prior numbers. (Henao, Clewlow and Mishra). I would argue that these effects are also transferrable to an individual ownership model AV, and the significant piece here is that having a private driver induces significant travel demand

## Slide 10: FLEET VS. INDIVIDUAL OWNERSHIP
  Main difference being that the downtime for fleet vehicle is significantly less than the 95% downtime of an individually owned vehicle
  Lose benefits of storing things in your car/tailoring preferences
  Expect significantly less GHGs with fleet vehicle due to reduction in manufacturing emissions
  Fleet model not applicable to rural areas, possibly suburban areas
  Reviewed literature to find a replacement calculation of 6.7:1 based on VMT of Taxi fleets (NHWTA 2017, Fournier et al. 2017)
bu.edu/ise
Notes:   This is where a stock turnover model is really useful in gaining visibility into how to manipulate the total LDV fleet
  Fleet vs. Individual ownership
    Main difference being that the downtime for fleet vehicle is significantly less than the 95% downtime of an individually owned vehicle
  Lose benefits of storing things in your car/tailoring
  Expect significantly less GHGs with fleet vehicle due to reduction in manufacturing emissions (going to what Jim was saying yesterday, fleet vehicle travels 2-3x as far in its lifetime)
  Reviewed literature and ended up conducting a replacement calculation of 6.7:1 based on VMT of Taxi fleets -

## Slide 11: RAPID TURNOVER MODEL
  Thinking about AVs as comparable to technology improvements
  Reasons for:
    Cell phones and computers; battery improvement similar to other component cost improvements like semi-conductors
    Comfort and luxury updates are an incentive for manufacturing sales
  Reasons against:
    Cars are a relatively higher household expense now than computers were when they were first available; may be a different type of good
bu.edu/ise

## Slide 12
bu.edu/ise
GREENHOUSE GAS EMISSIONS IMPLICATIONS – LCA AND BUSINESS MODELS
Notes: So we took two cases from our previous paper – a policy case with things like a road tax and efficiency standards implemented, and a stress case, in which vehicles are allowed to

## Slide 13
bu.edu/ise
Notes: This is the policy case with EIA projections

## Slide 14
bu.edu/ise
Notes: Temporal: a) Who needs to plan for Evs over what period of time (will different areas need to plan more quickly) and b) will the load be added during the same hours in the day?
Spatial: What is load distribution now? I can imagine load centers are not currently evenly distributed; how will an increase in Evs change the spatial distribution of load?
AVs EVs? Evidence for no:

## Slide 15
Really difficult to reach the needed emissions reductions in the transport sector;
Three things that have an impact on emissions:
  electrification (charging infrastructure, policy incentives, battery density, drive train synergies)
  Decarbonization of the electric sector (renewable energy policy incentives)
  Manufacturing (business models, efficiency improvements)
PRELIMINARY TAKEAWAYS

## Slide 16
Migrating from one state to the next?
  E.g., from ICE to EV, from one business model to the next
AV computing and equipment load
Applying different VMT/EI effects to different business models?
Other thoughts?
ADDITIONAL CONSIDERATIONS