## Slide 1: Impact of Vehicle Automation on Electric Vehicle Charging Infrastructure Siting and Energy Demand
Avi Chaim Mersky
(Amersky@alumni.cmu.edu)
Constantine Samaras
Carnegie Mellon University
Department of Civil and Environmental Engineering
Economics of Autonomous and Electric Vehicles
The National Bureau of Economic Research
Friday, June 7, 2019

## Slide 2: Agenda
Why this Matters
How Vehicle Automation May Affect EV Charging
Trip Characteristics and Charger Selection
Optimization Methods
Results
Implications
Limitations and Future Work

## Slide 3: Transportation is Now The Largest Source of U.S. GHG Emissions
Source: https://www.epa.gov/ghgemissions/sources-greenhouse-gas-emissions

## Slide 4: Transportation is Hard to Decarbonize
Data: DOE, Image by Abdullah Alarfaj, CMU

## Slide 5: Low-Carbon Electricity Can Enable Deep GHG Reductions with EVs
Chart: Grid CO2 Intensity g CO2 / kWh
| 600 | 500 | 400 | 300 | 200 | 100 | 0
kg / mi 0.3 kWpg EV | 180 | 150 | 120 | 90 | 60 | 30 | 0
kg / mi 30 mpg ICV | 300 | 300 | 300 | 300 | 300 | 300 | 300
0.3 kWh / mi EV
30 mpg ICV

## Slide 6: Oil Use Accounts for 39% of Transportation Externalities
Oil Security (21 ¢ )
Air Pollution (49 ¢ )
Climate Change (59 ¢ )
Congestion ($1.46)
Crashes (63 ¢ )
Noise (3 ¢)
39%
Source: Updated from Anderson et al., 2014, Uses NHTSA 2017-2025 Estimates, updated SCC Costs,
GREET WTW emissions, assumes 25 mpg, $2013
Notes: Et. Al includes Costa
Source is DOT/Nhtsa

## Slide 7: However, Public Charging Stations can be Expensive
Cost for a single vehicle 240 volt charger installed can vary between $4,000 and $20,000
DC Fast charging can cost between $40,000 and $90,000
Source: Smith, M., and Castellano, J. (2015).

## Slide 8: It is Challenging to Reduce EV Charging Infrastructure Costs
Vehicles take up the chargers physical space and ports until someone moves/disconnects them
Vehicles need to either charge near the driver’s destination or must charge in comparable times to gasoline pumps
Level 4 & 5 automation could allow for a reduction in the number of necessary chargers

## Slide 9: What We Mean When We Say Level “X” AV
Level | Name | Who is Driving? | Who is Monitoring? | Who Intervenes?
0 | No Automation | 😀t | 😀t | 😀t
1 | Driver Assist | 😀🤖 | 😀t | 😀t
2 | Partial Automation | 🤖😀t | 😀t | 😀t
3 | Conditional Automation | 🤖t | 🤖t | 😀t
4 | High Automation | 🤖t | 🤖t | 🤖😀
5 | Full Automation | 🤖t | 🤖t | 🤖t
Source: Adapted from NHTSA and SAE J3016

## Slide 10: Research Question
How can the various levels of vehicle automation affect the economics and energy use of charging EVs?

## Slide 11: How Vehicle Automation may Affect EV Charging
Level 0-3 Automation
  The charger is occupied until the commuter moves it.
  The commuter must walk from the parking spot to their destination and back

## Slide 12: How Vehicle Automation may Affect EV Charging
Level 4 Automation
  The vehicle can move itself on and off the charger
  The commuter must still walk after parking
Level 5 Automation
  The vehicle can move itself on and off the charger
  The vehicle and drop off and pick up the commuter
https://www.pluglesspower.com/learn-about-plugless/
https://www.media.volvocars.com/global/en-gb/media/pressreleases/49569/photos
Notes: Level 3 would require supervision

## Slide 13: Data and Methods
We investigated King County, Washington
We used the 2014 Puget Sound Household travel survey data directly
Source: Google Maps

## Slide 14: Trip Characteristics
2,300 trips Total
1,900 parking spaces demanded during peak hour
Max possible modeled charger utilization is 31%
  Based on commuter distances and charge switching time

## Slide 15: Most Drivers in the Sample Commute Short Distances
Source: 2014 Puget Sound HHTS

## Slide 16: Almost All Sampled Commuters Park Long Enough to Fully Charge
Source: 2014 Puget Sound HHTS

## Slide 17: Charger Selection
AC Level 1 / 120 V Charging
  About 5 miles per hour
  <$2,000 (significantly less for new construction)
AC Level 2 / 240 V Charging
  About 20 miles per hour
  About $10,000 per charger
DC Fast Charging
  About 150 miles per hour
  About $50,000 per charger
Notes: Level 1 is not demand risk robust
DC is much too expensive per mile of charge
For charging while parked scenarios

## Slide 18: Costs are Evaluated for Charger Station Owners as well as Drivers
Charger Owner Costs
  Real Estate
  Amortized Capital Equipment and Installation Costs
    Number of Chargers
    15 years with a 4.1% discount rate
Driver Costs
  Walking
    Derived from median income and time
  Additional Vehicle Depreciation and Energy Costs
Notes: Discount rate from city bond rates

## Slide 19: King County Assessed Real Estate Prices
Notes: Darker more expensive per square foot

## Slide 20: Optimization Methods
We know when each commuter arrives and leaves each Travel Analysis Zone (TAZ)
We assume each commuter will drive an electric vehicle
We want to minimize the total costs of Drivers and Charger Owners

## Slide 21: Optimization Methods
Level 0-3 Automation (No Self-Driving Vehicles)
  Minimize the total costs of walking and charger owners
  One charger is required for every peak vehicle
  Max walking distance of 0.25 miles

## Slide 22: Optimization Methods
Level 4 automation (Self Parking and Charging Vehicles)
  Same as Level 0-3 but chargers can now serve multiple vehicles
    Vehicles can queue up to as charger with a one minute switching time after charging is finished
    Max walking distance of 0.25 miles

## Slide 23: Optimization Methods
Level 5 Automation (Completely Self-Driving and Charging Vehicles)
  Decouple commuter destination from parking location
  Vehicles energy and depreciation costs are ~20 times less per mile than walking

## Slide 24: Results: Level 0/No Automation
$1.75 M Total Costs
  Almost all is charger owner because of single charger per vehicle and max walking distance constraint
1,900 Chargers
  1.2 trips per charger
  4.4% Utilization
    Time that the charger is actually used

## Slide 25: Results: Level 4 Automation
$930,000 Charger Owner
$940,000 Total Costs
  Commuter costs remain bounded by walking distance
680 Chargers
  3.5 Trips per charger
  13% Utilization
Notes: 50% Price Decrease

## Slide 26: Results: Level 5 Automation
$440,000 Charger Owner
$540,000 Total Costs
  Commuter Costs increased by a factor of 10
330 Chargers
  7.5 Trips per charger
  27% Utilization
Notes: Additional 50% price decrease

## Slide 27: Reduction in Number of Chargers: Level 0-4 Vehicle Automation

## Slide 28: Reduction in Number of Chargers: Level 0-5 Vehicle Automation

## Slide 29: Automation Enables Demand Smoothing
Assume 35 kWh / 100 mi
Chart: Hour
| 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
AV 0-3 | 663.0225 | 1442.2275 | 2061.4825 | 1399.6605 | 703.92 | 340.361 | 212.7195 | 230.9405 | 160.566 | 193.3155 | 146.132 | 96.019 | 69.51
AV 4 | 821.24 | 1430.4913 | 1430.4913 | 1430.4913 | 1227.9876 | 309.883 | 201.25 | 227.4615 | 181.601 | 187.6175 | 146.0655 | 98.3395 | 55.335
AV 5 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 668.5756 | 338.5879 | 55.335
Notes: Moving from levels 0-3 to level 4 automation reduces the peak electrical demand by 31%
Moving from levels 0-3 to level 5 reduces the peak electrical demand by 68%,
AV4 could be accomplished with smart charging with different equipment and some restrictions on number of vehicles per spot

## Slide 30: Implications
Optimizing EV infrastructure for AVs enables smoothing of peak EV electric demand
Similar results could be gained through smart charging technology
  Though those have their own cost structures and technical limitations

## Slide 31: Implications
Automation allows for considerable decreases in the total chargers and charger owner cost
  Number of chargers reduced from 1,900 to 330
  $1.8 M to $440,000
But shifts a portion of the costs to commuters
    How do we best incentivize the social good without harming travelers?
Notes: 80% reduction in number of chargers

## Slide 32: Limitations
Traffic demand taken direct from HHTS
  Demand is shown to be more concentrated than reality
  Demand is much smaller than reality
Poor real estate data
Notes: No demand regression or modeling
Limits ability to take advantage of increased utilization from Level 4 Avs
Over estimates needed infrastructure of no AVs

## Slide 33: Questions?

## Slide 34: Appendix Slides

## Slide 35: Data Sources
Infrastructure Costs
  DOE Report
GIS Data and Trip Distribution/Characteristics
  Puget Sound Household Travel Survey
  Census Bureau
  King County GIS

## Slide 36: Commuter Arrival and Departure Times

## Slide 37: Reduction in Number of Chargers: Level 4-5 Vehicle Automation

## Slide 38: Optimization Detailed
Notes: City of Seattle’s current 4.122% 30-year bond rate

## Slide 39: No Automation (Level 0-3 AV)
Objective:
Decisions:
  peak parking demand of zone i served in location j, (stations to build in j), integer
What we Want:
Constraints:
  (all parking demand served)
  (non-negativity constraint on parking demand)
  (non negative station assignment)
  (maximum walking distance)
Given:
  cost)
  (walking costs)
  (binary check if anyone walked between i and j)
Input Parameters:
  costs per charging station, equipment and installation, $
  walking distance between zone i and location j, miles
  cost of walking, $ / mile
  maximum walking distance, miles
  average number of trips per peak trip in zone i, can be fractional, count
  annuity value of current lump sum, $

## Slide 40: Self Parking (level 4 AV)
Objective:
Decisions:
  total trips ending in zone i served in location j, count
What we Want:
  , integer
Constraints:
  (all parking demand served)
  (non-negativity constraint on parking demand)
  (maximum walking distance)
Given:
  cost)
  (walking costs)
  (binary check if anyone walked between i and j)
  zone charge capacity, miles
Input Parameters:
  miles
  mean trip distance for trips ending in zone i, miles
  real estate cost per parking space and charger at location j, $
  costs per charging station, equipment and installation, $
  walking distance between zone i and location j, miles
  cost of walking, $ / mile
  maximum walking distance, miles
  charger utilization rate, %
  charger capacity, miles per shift
  annuity value of current lump sum, $

## Slide 41: Self Driving (Level 5 AV)
Objective:
Decisions:
  total trips ending in zone i served in location j, count
What we Want:
Constraints:
  (all parking demand served)
  (non-negativity constraint on parking demand)
  (non-negative station assignment)
Given:
  cost)
  (drop-off/pick-up energy cost, $)
  (binary check if anyone walked between i and j)
  zone charge capacity, miles
Input Parameters:
  miles
  mean trip distance for trips ending in zone i, mile
  real estate cost per parking space and charger at location j, $
  costs per charging station, equipment and installation, $
  walking distance between zone i and location j, miles
  charger utilization rate, %
  charger capacity, miles per shift
  fuel economy, kWh / mi
  price of electricity, $ / kWh
  annuity value of current lump sum, $
  cost of wireless AV communication equipment maintenance, $ / year