## Slide 1: A Blended Data Approach to Measuring Monthly Housing Starts: Satellite Imagery, Survey Data and More!
Nikki Czaplicki
U.S. Census Bureau
Any opinions and conclusions expressed herein are those of the authors and do not reflect the views of the U.S. Census Bureau.

## Slide 2: Meet the team
U.S. Census Bureau
Nikki Czaplicki
Aidan Smith
Scott Springer
Reveal Global Consulting
Hector Ferronato
Dwarakh V. Nayam
Lei Peng
Colin Shevlin
Doren Walker

## Slide 3: Re-engineering housing start estimation
Goal: Combine traditional survey collected data with estimates derived from satellite imagery to produce a hybrid estimate of monthly single-family housing starts
The Census Bureau has reviewed this product to ensure appropriate access, use, and disclosure avoidance protection of the confidential source data (Disclosure Review Board (DRB) approval number: CBDRB-FY25-0086).

## Slide 4: Current Construction Indicator
New Residential Construction (NRC)
  commonly referred to as “Housing Starts”
  provides monthly national and regional estimates of housing units started, authorized but not started, under construction and completed.
  sources data from Survey of Construction (SOC)
    Sampling of building permits authorizing new, privately-owned residential construction
    Physical canvassing of areas not requiring building permits
Data Users
  BEA, Federal Reserve, Council of Economic Advisors, Department of Housing and Urban Development, Manufacturers, Insurance Companies, Financial Institutions

## Slide 5: Three Stage Sampling
Subsample of Current Population Survey Primary Sampling Units (PSUs)
Selection of Permit/Non-Permit Areas
Monthly Selection of Permits
*Note: Map for illustrative purposes and does not reflect SOC sample

## Slide 6: Observing Starts
Current | Re-engineered
Field representative interviews | Satellite imagery for selected places from the existing SOC sample. ML models identify construction activity. Field collection for remaining places.
Sampled permits only | All projects in the selected place can be observed (no longer sampling projects).
Burdensome for respondents - can require multiple interviews to get a start date for a project that does not start right away | Respondent contact no longer needed to capture the start

## Slide 7: Satellite Areas of Interest (AOIs)
Select AOIs that are dense in new residential housing starts.
Identify boundaries using Census TIGER*/Line shapefiles.
Provide image broker with augmented shapefiles.
  Simplify
  Combine
  Exclude
Images captured in 10-day window (End of month ±5 days)
*Topologically Integrated Geographic Encoding and Referencing system

## Slide 8: Developing a Construction Stage Model
Identify construction stages present in satellite imagery
Background
Land
Vegetation
Excavation
Foundation
Framing
Unfinished Roof
Finished Roof

## Slide 9: Construction Stage Labeling

## Slide 10: Construction Stage Predictions
LAND
VEGETATION
EXCAVATION
FOUNDATION
FRAMING
ROOF

## Slide 11: Parcel Limitations
Outdated geometry
Incomplete data
Inaccurate zoning information

## Slide 12: Identifying Starts Through Blob Search

## Slide 13: Interpreting Starts With Business Rules
 |  | Current Month Prediction |  |  |  |  |  |  | 
 |  | Background | Land | Vegetation | Excavation | Foundation | Framing | Unfinished Roof | Roof
Previous Month Prediction | Background | Unknown | Land | Land | Start | Start | Start | Start | Start Completion
 | Land | Land | Land | Land | Start | Start | Start | Start | Start Completion
 | Vegetation | Land | Land | Land | Start | Start | Start | Start | Start Completion
 | Excavation | Image Error | Land | Land | In Progress | In Progress | In Progress | In Progress | Completion
 | Foundation | Image Error | Misclassified Backwards | Misclassified Backwards | In Progress | In Progress | In Progress | In Progress | Completion
 | Framing | Image Error | Misclassified Backwards | Misclassified Backwards | In Progress | In Progress | In Progress | In Progress | Completion
 | Unfinished Roof | Image Error | Misclassified Backwards | Misclassified Backwards | In Progress | In Progress | In Progress | In Progress | Completion
 | Roof | Image Error | Misclassified Backwards | Misclassified Backwards | Start Reconstruction | Start Reconstruction | Start Reconstruction | Start Reconstruction | Exist

## Slide 14: Developing a Building Type Model
Classify areas by likely building type
Single-family detached
Single-family attached
Multi-family
Non-residential
Background

## Slide 15: Building Type Labeling

## Slide 16: Building Type Model Predictions
Background
Single Family Detached
Non-Single Family

## Slide 17
Blue shape indicates a building footprint
Black shape indicates a start prediction
Building Footprint Exclusion
Utilize open-source building footprint data to reduce noise.
Overlay start blobs on footprint shapes and exclude overlaps as probable noise.
Similar procedure performed using TIGER/Line road data.

## Slide 18: Imputation of satellite data
Missing data in the satellite image due to cloud cover
Construction is not evenly distributed across the AOI – place level missing data adjustment not appropriate
Divide the AOI into its component 7-character Geohashes (153m x153m) and impute/adjust at the Geohash level

## Slide 19
)
Cloud Coverage < 50%
Cloud Coverage >= 50%
Imputation – Scenario specific methods

## Slide 20: Capture Window Adjustment
April |  |  |  |  |  | 
Sun | Mon | Tue | Wed | Thu | Fri | Sat
31 | 1 | 2 | 3 | 4 | 5 | 6
7 | 8 | 9 | 10 | 11 | 12 | 13
14 | 15 | 16 | 17 | 18 | 19 | 20
21 | 22 | 23 | 24 | 25 | 26 | 27
28 | 29 | 30 |  |  |  | 
Prior month image obtained
Current month image obtained
Ideal scenario
April |  |  |  |  |  | 
Sun | Mon | Tue | Wed | Thu | Fri | Sat
31 | 1 | 2 | 3 | 4 | 5 | 6
7 | 8 | 9 | 10 | 11 | 12 | 13
14 | 15 | 16 | 17 | 18 | 19 | 20
21 | 22 | 23 | 24 | 25 | 26 | 27
28 | 29 | 30 |  |  |  | 
Possible real-world scenario
30 days between images
25 days between images
Capture window adjustment:
Adjusted starts =

## Slide 21: Satellite data process flow
Obtain satellite images
Predict construction stages and building type
Include only areas predicted as single family by the building type model
Exclusions based on building and road footprint overlap
Imputation for obscured areas
Capture window adjustment
Final place level satellite estimate
Final place level satellite estimate
𝑠_(𝑝,𝑡)
Apply business rules to identify starts
Blob search
Obtain satellite images
Predict construction stages and building type
Include only areas predicted as single family by the building type model
Exclusions based on building and road footprint overlap
Imputation for obscured areas
Capture window adjustment
Apply business rules to identify starts
Blob search

## Slide 22
Survey Estimate
Satellite Estimate
Blended Estimate

## Slide 23: Estimation – current state
Building Permits Survey (BPS) permits for month
survey estimate of permits authorized in month
urvey estimate of starts in month , authorized in month
, if unit started in month , 0 otherwise.
https://www.census.gov/construction/soc/methodology.html

## Slide 24: Current State: Sample of permits from a place
 | Authorization Month |  |  |  |  |  | 
Start Month | Jan | Feb | Mar | Apr | May | Jun | July
Feb | Starts: 50 Auths: 100 | Starts: 50 Auths: 150 |  |  |  |  | 
Mar | Starts: 50 Auths: 100 |  | Starts: 100 Auths: 200 |  |  |  | 
Apr |  | Starts: 50 Auths: 150 |  |  |  |  | 
May |  |  | Starts: 100 Auths: 200 | Starts: 50 Auths: 50 | Starts: 50 Auths: 200 |  | 
Jun |  |  |  |  | Starts: 100 Auths: 200 | Starts:100 Auths: 250 | 
Jul |  | Starts:50 Auths: 150 |  |  |  | Starts: 150 Auths: 200 | 
Aug |  |  |  |  | Starts:50 Auths: 200 |  | Starts: 50 Auths: 250

## Slide 25: Satellite estimate of starts from a place
 | Authorization Month |  |  |  |  |  |  | 
Start Month | Jan | Feb | Mar | Apr | May | Jun | July | All Auth Months
Feb |  |  |  |  |  |  |  | 90
Mar |  |  |  |  |  |  |  | 160
Apr |  |  |  |  |  |  |  | 110
May |  |  |  |  |  |  |  | 250
Jun |  |  |  |  |  |  |  | 200
Jul |  |  |  |  |  |  |  | 190
Aug |  |  |  |  |  |  |  | 220

## Slide 26
Satellite estimate
Survey based estimate
Total estimate

## Slide 27: Primary sampling unit calibration weight
Compute non-satellite estimate of permits for each in sample PSU by summing
Compute the PSU calibration factor by dividing the BP total of permits from non-satellite place in the PSU by the non-satellite estimate of permits.
Multiply the PSU calibration weight by the SOC final weight to get the non-satellite final weight

## Slide 28: New estimator
= set of non-satellite places in SOC sample
BPS permits for non-satellite places for month
survey estimate of permits authorized for non-satellite places in month ,
survey estimate of starts in month , authorized in month for non-satellite places,
https://www.census.gov/construction/nrc/pdf/satellite_edp_methodology.pdf

## Slide 29: Keep SOC methodology for non-satellite component
Nonresponse – compute nonresponse undercoverage adjustment factors (NUAFs) from the SOC data at the division level excluding satellite places
Variance estimation
  Continue to use modified half-sample to estimate sampling variance with a modification to the way replicate weights are assigned to permits from non-self-representing PSUs
  Satellite places we have selected so far are self representing and do not contribute to the sampling variance estimate

## Slide 30: Published Estimates
Survey Month | Experimental Data Product Release 11:00 am
November 24 | December 19, 2024
December 24 | January 21, 2025
January 25 | February 20, 2025
February 25 | March 19, 2025
March 25 | April 18, 2025
April 25 | May 19, 2025
May 25 | June 20, 2025
June 25 | July 21, 2025
July 25 | August 20, 2025
August 25 | September 18, 2025
September 25 | October 20, 2025
October 25 | November 20, 2025
November 25 | December 17, 2025
https://www.census.gov/construction/nrc/data/satellitestarts.html

## Slide 31: Research & Development
Geographic Expansion
Currently tasking additional AOIs to construct an estimate for South region.
Improved Single-Family Attached
Develop techniques to better quantify single family attached vs detached starts.

## Slide 32: Research & Development
Widespread cloud coverage impacts ability to predict.
Early development of modeling solutions.
Dynamic capture windows using weather forecasts.

## Slide 33: Future Work
Multi-Family Construction
Additional SOC
Data Items
Starts
Under
Construction
Completions

## Slide 34: Questions?
Contact us at:
Nicole.Czaplicki@census.gov
eid.nrc.satellite@census.gov